Controller Design SMIB

by Direct Feedback Linearization

Tamaji, Musyafa A, Agus Darma, Imam Robandi

e-mail : tamajikayadi@yahoo.com

Department of Electrical Engineering , Faculty of  Industrial Technology

Sepuluh Nopember Institut of Technology, Campus ITS Sukolilo Surabaya 60111

Abstract -- Single machine infinite bus is a non linear dynamic system. To design the controller of non linear dynamic system is not easy. Usually, we linearize the system and after that design the controller as linear dynamic system. In this paper, we studied the controller design of single machine infinite bus (SMIB) by using a direct feedback linearization (DFL). This method is different with  linearization method by Taylor series approximation. Here, we did simulation by Matlab program. From this simulation, we know that DFL method can be applied to design the controller of SMIB.

Keywords: SMIB, DFL, design controller

- Introduction

Controller design is a method to determined of feedback gain such that the system become closed loop system and has the desired pole. Usually, the controller design is done to make the system stable or place the pole in the left half plane. Design controller, usually is applied in the linear dynamic system, so that for non linear dynamic system, we must linearize before we design the controller.

In this paper, we design the controller of power system with single machine infinite bus (SMIB) by using direct feedback linearization (DFL). The DFL method consist of two steps: the first one is compensator linearization of non linear state feedback variable DFL (output) which change the non linear system become linear system with new input, and the second is optimal control design non linear [1]. Before we applied the DFL method, we derive the mathematical model of power system with SMIB.

- Dynamic Model of SMIB

Single machine infinite bus is a simple model of power system [2]. This system consist of single power which connect with two line parallel transmission respect to large networking and approximate by infinite bus. This system is showed in Figure 1.

Figure 1. SMIB power system

Mathematical model of this system, consist of mechanic equation, power electric equation and electrical equation. The mathematical model  [1] are:

Mechanical equation is

(1)

(2)

Electric power dynamic

(3)

Electrical equation

(4)

(5)

(6)                        (7)

(8)

(9) Equation (1) –(8) are SMIB mathematical model. Where  is rotor angel,  is a rotor velocity,  reference velocity, , is mechanical power input and  active power delivery, respectively.  is a damping power coefficient, is internal transient power, is a transient reactance and synchronize transient. is stator current in direction d and q,   is excitation amplifier from gain and control input.  is a infinite voltage and power terminal voltage.  is a reactive power delivery .

The DFL method is beginning by differentiate  the active power delivery  Eq. (6) respect to time, we get

or

(10)

Substitute Eq. (3, 8,9) into Eq. (10),  the equation (10) become

(11)

We arrange Eq. (11), and we get

And finally we have

(12)

Define , from Eq. (1),(2) and (12) we have the linear dynamic system of SMIB with input :

(13)

Where

Equation (13) can be written as state space system

(14)

Now, the problem is design a controller such that system (14) stable asymptotical.

- Control Design Law DFL

Define an input system [1]:

(15)

for  in  .

In the system Eq.(14)  are  desired  converge to.

Suppose

(16)

Where   is feedback gain, then system (14) become

(17)

Therefore, we must determine feedback gain  such that system (17) asymptotical stable [3].

Here we use pole assignment method to determine feedback gain F.

After we obtained  then we substitute those value in Eq. (16) to get new input  , and then this value is substitute to Eq. (15) to get the real input .

- Simulation Result

To make a simulation, we take the parameter from [3]:

For pole placement method, we take some poles and we obtain the feedback gain by using Matlab function (place) [3]. Figure 2. Shows system SMIB without input controller system is unstable.

Figure 2. SMIB without control

Case 1. For case 1, we take pole=[-1;-2;-0.5] and  by Matlab program, we get feedback gain

F=[   -0.1763   -1.3002   20.8375].

For this feedback gain, the performance of SMIB is stable (Figure 3a), the new input  is shown in Figure (3b) and the real input control u in Figure (3c).

Figure 3a. SMIB with control input

Figure 3b. The new input

Figure 3c. control input u

Case 2: For case 2, we take pole=[-5;-10;-3]; and by Matlab program we get  feedback gain     F=[-26.4402  -15.8313  120.8875]

In this case the system is stable, the state of system, new input  and control input u, are represented in Figure (4a),(4b),(4c).

Figure 4a. SMIB with control input

Figure 4b.  The new input

Figure 4c. Control input u

Case 3. For pole=[0;-1;-2]; and we get  F=[0.0000   -1.0909   17.3875]; The SMIB system is unstable. The performance, the new input and control input are represented Figure (5a),(5b), and (5c)

Figure 5a. SMIB system with control

Figure 5b. Control input

Figure 5c. Control input u

From those figures, we know that the SMIB system without control input is unstable. The case 3, feedback gain F=[0.0000 -1.0909   17.3875] is an example of system with control input u(t), but system is still unstable. This is happen because control feedback system Eq.(17)  has pole zero.

- CONCLUDING REMARK

From our analyze and simulation we conclude that

  - The DFL method can be applied to design the controller of SMIB

  - The feedback gain of linear system is determined by function in Matlab

  - The second case, F=[-26.4402  -15.8313  120.8875]  give a good performance, the state is stable with smooth performance, without oscillation.

Bibliography

- Yadaiah, N., Ramana, NY,2006, Linearization of multi machine power system: Modeling and control

- Imam Robandi, 2006, Desain Sistem Tenaga Modern, Penerbit Andi

- Ogata, K., 1997, Modern Control Engineering, Prentice Hall.